## Slide 2
CHAPTER 1.
INTRODUCTION

## Slide 3: FIXED SPECTRUM ASSIGNMENT

## Slide 4: Fixed Spectrum Utilization
Maximum Amplitudes
Amplitude (dBm)
Heavy Use
Heavy Use
Medium Use
Sparse Use
Frequency (MHz)

## Slide 5: Fixed Spectrum Utilization
GHz
PSD (Power Spectrum Density)
Freq (GHz) | 0~1 | 1~2 | 2~3
Utilization(%) | 54.4 | 35.1 | 7.6
3~4 | 4~5 | 5~6
0.25 | 0.128 | 4.6
Measurements show that there is wide range of spectrum utilizations
across 6 GHz of spectrum

## Slide 6
Problems of Fixed Spectrum Utilization
Spectrum usage is concentrated on certain portions of the spectrum
A significant amount of the spectrum remains unutilized.
According to FCC (Federal Communication Commission):
Utilization of the fixed spectrum assignment is approx.
15-85% based on temporal and geographical variations
 Limited Available Spectrum and Inefficient Spectrum Usage!

## Slide 7: COGNITIVE RADIO NETWORKS; DYNAMIC SPECTRUM ALLOCATION NETWORKS (DSANs); xG INITIATIVE
Dynamic Spectrum
Allocation

## Slide 8: OVERALL VIEW
Dynamic Spectrum
Allocation
Applications
TCP/UDP
IP
MAC
Error Control
Physical
Adaptive
Protocol
Suite
Wireless LANs & MANs
Cellular
(2,3,4-G)
Mesh Networks
Sensor
Networks
WiMAX

## Slide 9
A “Cognitive Radio” is the key enabling technology for Dynamic Spectrum Access!!
Capability to use or share the spectrum in an opportunistic manner.
“BANDWIDTH HARVESTING”
Dynamic spectrum access techniques allow the CR to operate in the
best available channel.
COGNITIVE RADIO

## Slide 10
1) Determine which portions of the spectrum is available and detect the
presence of licensed users when a user operates in a licensed band
(Spectrum Sensing)
2) Select the best available channel (Spectrum Decision)
3) Coordinate access to this channel with other users (Spectrum Sharing)
4) Vacate the channel when a licensed user is detected
(Spectrum Mobility).
SPECTRUM MANAGEMENT FRAMEWORK

## Slide 11: COGNITIVE RADIO NETWORK COMMUNICATION FUNCTIONALITIES
Spectrum
Mobility
Function
Spectrum
Decision
Function
Sensing Information / Reconfiguration
Handoff Decision, Current and Candidate Spectrum Information
QoS Requirements
Reconfiguration
Routing Information/
Reconfiguration
Routing Information
Handoff Delay, Loss
Scheduling
Information/
Reconfiguration
Sensing
Information
Application Control
Link Layer
Delay
Link Layer
Transport
Network Layer
Physical Layer
Application
Spectrum
Sensing
Spectrum
Sharing